## Slide 1: PowerPoint 2: Units and measurement
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
describe the key units of electrical quantity
explain Ohm’s law
explain the difference between and significance of energy and power
explain how current and resistance are measured
describe the function of capacitors and inductors
understand the difference between direct current (DC) and alternating current (AC).

## Slide 3: Electric circuit theory
We are already familiar with the terms voltage, current and resistance. They are represented in the following circuit.
+
-
V or emf
I
R
Potential difference
A potential of 1V appears across a resistance of 1Ω when a current of 1A flows through that resistance.

## Slide 4: Potential difference with more than one resistor
Potential difference is the voltage drop across a component. It is measured between two points either side of the component. We describe this as the potential difference measured across a component. V1, V2 and V3, shown below, are potential differences.
R1
R2
R3
V1
V2
V3
V
I

## Slide 5
Ohm’s law
In 1827, George Ohm found that whenever current flows in an electrical circuit the pressure (potential difference) between the ends of the circuit is proportional to the current flowing through the circuit.
Thus, V α I or V = kI
where k is a constant.
In our case, the constant is called resistance,
designated by the letter R.
V = IR
OR current = voltage/resistance
I = V/R

## Slide 6
Current (unit – amp, short for ampere, A): the measure of the rate at which electricity flows past a given point in an electric circuit. With 1A of current 6.24 x 1018 electrons flow per second.
Quantity (unit coulomb, C): since the ampere is the measure of the rate of flow of electricity it follows that the quantity of electricity depends on both the rate of flow and the time it is flowing. Unit quantity of electricity is therefore defined as the quantity of electricity passing a point in a circuit when a current of 1A flows for 1 second (s).
1C = 6.24 x 1018 electrons = 1A per s
I =
Amps and coulombs

## Slide 7: Work or energy (joules)
Joules (J) are the measure used to describe the work done or energy expended when 1C (coulomb) of electricity is passed through a resistance of 1Ω.
Consider a conductor through which quantity of current Q is passing in time t and let the potential difference between two ends of wire be V.
The energy in joules (J) = V x Q
W = V x Q
Remember: V = IR
W = (IR) x Q
Q = It
W = IR x It
W = I2Rt

## Slide 8: Power (watts)
Power is defined as the rate of doing work. Since the unit of work is the joule, it follows that the unit of power is a joule per second (J per s),known as a watt (W).
Since work done in a circuit = I2Rt J
then power expended = I2Rt/t = I2R W
From Ohm’s law I = V/R
So power = V2/R

## Slide 9: Measuring voltage, current and resistance
Routine electrical test work involves measuring current, voltage and resistance, ie amps, volts and ohms. This is most conveniently done using a multimeter with all the necessary functions and ranges. The instrument has a digital display and can be auto-ranging (it automatically sets the correct range for the value of the variable).

## Slide 10: Measuring voltage
With the multimeter held across the component, it will measure the difference in voltage.
R1
R2
R3
V1
V2
V3
V
I
V1

## Slide 11: Measuring current
To measure current, the multimeter has to be connected in series with the component.
R1
R2
R3
V
I
I

## Slide 12: Measuring resistance
When measuring resistance, the supply must be switched off and the component under test is usually removed from the circuit – this avoids any errors if other components are also connected in parallel.
R1
R2
R3
R

## Slide 13: Capacitors
A capacitor stores energy, producing a potential difference across the component itself. It acts like a rechargeable battery.
In its basic form, a capacitor consists of two plates. They are electrically separated by an insulator. This insulating layer between the plates is called the dielectric.
Symbol
Capacitor

## Slide 14: Understanding capacitors
When used in a direct current (DC) circuit with a battery, a capacitor charges up to its supply voltage but then the flow of current stops. When a capacitor is connected to an alternating current (AC) circuit with a transformer, the flow of current appears to pass straight through the capacitor with little or no resistance. You will see later what the resistance to current in an AC circuit is for a capacitor.
When applying a voltage across the capacitor, the ratio of the charge Q to the voltage V will give the capacitance value of the capacitor and is therefore given as: C = Q/V.
Therefore the quantity of charge on the plates is: Q = C x V
The energy stored in a capacitor is: W = 1/2CV2

## Slide 15: Capacitance
The unit of capacitance is the farad (F).
A capacitance of 1F exists when a charge of 1C (coulomb) is stored on the plates by a voltage of 1V. However, the farad is a very large unit of measurement to use on its own, so sub-multiples of the farad are generally used such as microfarads, nanofarads and picofarads.
Standard units of capacitance
Microfarad (μF) 1μF = 1/1,000,000 = 0.000001 = 10-6 F
Nanofarad (nF) 1nF = 1/1,000,000,000 = 0.000000001 = 10-9 F
Picofarad (pF) 1pF = 1/1,000,000,000,000 = 0.000000000001 = 10-12 F

## Slide 16: Connecting capacitors together in series and parallel
The total capacitance, CT, can be calculated when connecting multiple capacitors in series and parallel.

## Slide 17: Inductors
An inductor is an electronic component that stores energy in the form of a magnetic field. It is a coil of wire that can be wound around a material. The inductor has units of inductance called the Henry (L). The inductance depends on the radius of the coil and on the type of material around which the coil is wound.

## Slide 18: Energy in an inductor
When a current is applied to a coil, a magnetic field is created.
The magnetic field surrounding an inductor stores energy as current flows through the field. When the current is reduced the magnetic field reduces, releasing the stored energy.
W= LI2

## Slide 19: DC
DC is an abbreviation of direct current. In DC circuits, the voltage is constant and the polarity does not change, resulting in current flow in one direction. A battery is a source of DC.

## Slide 20: AC
AC is an abbreviation of alternating current. In AC circuits, the voltage changes from positive to negative over a period of time resulting in the current changing from positive to negative over the same period. This means the current changes direction periodically in the circuit. An alternator (AC generator) is a source of AC current.

## Slide 21
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.