## Slide 1: PowerPoint 4: Resistors, capacitors and inductors
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
understand the function of resistors, capacitors and inductors in DC circuits.

## Slide 3: Operation of a resistor and capacitor in series
Switch open
R
C
E
Consider the circuit shown. The switch is open and the capacitor is completely discharged.
VR = 0V
VC = 0V
VR
VC

## Slide 4
Switch closed
R
C
V
I
The switch is now closed.
The initial current is only limited by the resistance in the circuit as the capacitor was initially fully discharged: I = V/R.
The capacitor will now start to charge up.
The potential difference across the capacitor VC will now increase.
At the same time the potential difference across the resistor VR will decrease.
After a period of time the capacitor becomes fully charged and the current will stop.
VR
VC

## Slide 5
Switch closed
R
C
V
I
I
t (s)
I = V/R
When the switch closes, the current instantaneously increases to I = V/R.
As the capacitor charges up the current reduces exponentially. After a period of time the current is zero.

## Slide 6
t (s)
Vc
V
When the switch closes, the potential difference VC across the capacitor is initially zero as it offers no resistance to current – therefore, VR = V. As time progresses the capacitor then charges up so the potential difference VC across it increases. The potential difference VR across the resistor decreases.
VR
Remember from Kirchhoff’s law: V= VR + VC

## Slide 7
The time it takes the capacitor to fully charge VC = V is dependent on the circuit components.
This is called the time constant of the circuit, symbol Ꞇ (tau) seconds.
Ꞇ = C x R
It takes approximately 5Ꞇ seconds for the circuit to fully charge.
The value of each of the circuit variables can also be calculated at any point from t = 0 seconds to t = 5Ꞇ seconds.
The circuit variables have changed by 63.2% when t = 1Ꞇ.

## Slide 8
I
t (s)
I = V/R
t (s)
Vc
V
VR
)
vR)
vC)
1τ
1τ
63.2% fall
1τ
63.2% fall
63.2% rise

## Slide 9: Example
A 40uF capacitor is connected in series with a 1kΩ resistor across a 50V DC. supply.
Calculate
The circuit time constant
The voltage across the capacitor after 60ms
The circuit current after 60ms
The time taken for the capacitor voltage to reach 20V
Approximate time taken for the current to fall to zero

## Slide 10: Solution
a) Ꞇ = C x R
= 40uF x 1kΩ = 40ms
b)
c)
(Or using Kirchhoff’s laws therefore = 11.2mA)
vC)
vC) = 38.84V
) and I = V/R therefore I = 50/1000 = 50mA
) = 11.2mA

## Slide 11: Solution
d)
vC)
)
ln
t = 20.43ms
e) Approx time for current to fall to zero = 5Ꞇ = 200ms

## Slide 12: Operation of a resistor and inductor in series
Switch open
R
L
V
VL
VR
Consider the circuit shown. The switch is open and the inductor and resistor are isolated.
VR = 0V
VL = 0V

## Slide 13
Switch closed
R
L
V
VL
I
The switch is now closed.
The initial current cannot rise instantly because of the self-induced electromotive force (emf) in the inductor L which opposes the voltage V.
The potential difference across the inductor VL = V.
At that point in time the potential difference across the resistor VR = 0V.
After a period of time the current will increase to a maximum limited only by resistance R so VL = 0V and VR = V.
VR

## Slide 14
t (s)
I
I = V/R
1τ
63.2%
When the switch closes the current is restricted by the induced emf in the inductor. As time progresses the current increases exponentially to a maximum limited only by resistance R.

## Slide 15
The time it takes the current to increase to a maximum I = V/R is dependent on the circuit components.
This is called the time constant of the circuit, symbol Ꞇ seconds.
Ꞇ = L/R
It takes approximately 5Ꞇ seconds for the current to reach its maximum value.
The value of each of the circuit variables can also be calculated at any point from t = 0 seconds to t = 5Ꞇ seconds.
The circuit variables have changed by 63.2% when t = 1Ꞇ.

## Slide 17
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.