## Slide 1: PowerPoint 5: AC circuits
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
demonstrate a thorough understanding of the basic principles of AC circuits.

## Slide 3: Generation of an AC waveform
A magnetic field rotates in the direction shown. As the field passes the fixed coil an electromotive force (emf) is created in the coil.
The magnitude of this emf depends on the position of the field.
The speed of rotation determines how quickly the voltage builds up. The poles of the field determine a positive-going voltage or a negative-going voltage.

## Slide 4: AC waveform

## Slide 5: Frequency- hertz
The time it takes for one cycle of waveform depends on the speed of the field.
This is the time period (T) of the waveform.
In the UK we generate 50 cycles a second.
This is called the frequency and the units are hertz (Hz).
So the time for one cycle = = 20ms.
Generally, f = 1/T.

## Slide 6: Relationship between voltage and current
With resistance only, the current reaches a maximum when the voltage reaches a maximum.
The current is in phase with the voltage in a purely resistive circuit operating at the same frequency.

## Slide 7: Voltage and current in a pure inductive circuit
In a DC circuit, the voltage across an inductor is maximum at t = 0s when the current is zero because of the effects of the induced emf. In an AC circuit the induced emf also causes the voltage and current to become maximum values at different times; however, they alternate at the same frequency.
The current is behind the voltage as time progresses.
Current lags the voltage by 90 degrees in a purely inductive circuit.
0O
90O
180O
270O
360O

## Slide 8: Voltage and current in a pure capacitive circuit
In a DC circuit the voltage across an capacitor is zero at t = 0s when the current is at maximum, because the capacitor is discharged. In an AC circuit the rate of change of supply voltage also causes the voltage and current to reach maximum values at different times; however, they alternate at the same frequency.
The current is in front of the voltage as time progresses.
Current leads the voltage by 90 degrees in a purely capacitive circuit.

## Slide 9: Phasor representation of a single phase voltage
Rotate @ angular velocity (
1 cycle = 2
f= 1/T
ω = 2 π f rads/sec
A sine wave can be represented by a phasor diagram.

## Slide 10: Phasors of V and I in a purely inductive circuit
V
V
I
I
Using a phasor diagram, we can represent the sine waves at any point in time. It shows the relationship between V and I and the angle between them. Since the phasor rotates in an anticlockwise direction, you can see that the current is lagging the voltage by 90 degrees. Similarly, a phasor could be drawn for a phasor relationship in a capacitive circuit showing the current leading.

## Slide 11: AC circuits: phasor diagrams
Resistive circuit: the voltage and current are in phase.
Inductive circuit: the current lags the voltage by 90 degrees.
Capacitive circuit: the current leads the voltage by 90 degrees.
V
V
V
I
I
I

## Slide 12
V AC @ f Hz
R
L
I
VR
VL
C
VC
V = VR + Vc + VL
Phasor diagram of RLC series circuit
The addition of the voltages are now considered phasor additions. This is indicated by the dash above the symbol.

## Slide 13: Phasor diagram of RLC series circuit
The voltage across each of the components is called a ‘phasor voltage’ and indicated by the dash above the symbol:
Adding them all together gives the total phasor voltage of the circuit.

## Slide 14: Resistance to current in an RLC circuit
VR = IR
The resistance to current in a pure inductive coil is called inductive reactance (XL), and its units are ohms. It is proportional to the angular frequency (ω).
XL = ωL= 2πfL Ω and VL = IXL
The resistance to current in a capacitor is called capacitive reactance (XC), and its units are ohms. It is inversely proportional to the angular frequency ω.
XC = 1/ωC= 1/2πfC and VC = IXC

## Slide 15: AC circuits
The resistance to current of the whole series circuit is called the impedance (Z) of the circuit and its units are ohms.
Z = in a RL series circuit
Z = in a RC series circuit
Z = in a RLC series circuit when XL > XC (lagging)
Z = in a RLC series circuit when XC > XL (leading)
and the circuit current would then be I = V/Z.
If the terms lag and lead are used to describe a circuit, they always refer to the current unless otherwise stated.

## Slide 16: Example
The following components are connected in series R = 10Ω, L = 50mH and C = 100uF.
They are connected across a supply of 240V, 50Hz.
We need to find out:
circuit impedance Z
circuit current I.
The solution and workings are shown on the next slide. The following slides show how we determine whether the circuit is leading or lagging.

## Slide 17
240V 50Hz
10Ω
50mH
I
VR
VL
100uF
VC
XL = 2πfL = 2π x 50 x 50mH = 15.71Ω
XC = 1/2πfL = 1/2π x 50 x 100uF = 31.83Ω
Z = = = 18.97Ω
a.
b.
I = V/Z = 240/18.97 = 12.65A
Example solution

## Slide 18
VR = 12.65 x 10 = 126.5V
VL = 12.65 x 15.71 = 198.7V
VC = 12.65 x 31.83 = 402.6V
VL = 198.7V
VR = 126.5V
VC = 402.6V
These voltages are phasor quantities, ie they have magnitude and direction. We can now add them and take into account the angles.
V = VR + VL + VC
VC and VL are direct opposites we have VC + VL as actually VC - VL.
VC - VL = 402.6 - 198.7
I = 12.65A
The current is the reference phasor as it is common to all components in a series circuit
Leading or lagging phasor diagram

## Slide 19
VL = 198.7V
VR = 126.5V
VC = 402.6V
VC – VL = 402.6 – 198.7 = 203.9V
V = VR + VL + VC
V = 240V
We can now add VR to the 203.9V
We know the supply voltage is 240 V so we can check our answer by using Pythagoras for a right-angled triangle.
= 240V
I = 12.65A
ϴ
Remember the phasor rotates anticlockwise so the current is leading the voltage by ϴ degrees.
Leading or lagging phasor diagram

## Slide 20: Power in AC circuits
True power P = I2RW
Consider the previous example: P = 12.652 x 10 = 1600W.
No true power is dissipated in the pure inductor or capacitor.
We can consider the supply voltage and supply current when calculating the true power but we have to take into account the angle between them.
The angle can be calculated from Pythagoras: = 58.2O
True power P = VIcosϴ = 240 x 12.65 x cos58.2 = 1600W
cosϴ is known as the power factor of the circuit and the angle must always be followed by lagging or leading.

## Slide 21
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.