## Slide 1: PowerPoint 6: Diodes and transistors
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
explain the properties and applications of diodes and transistors in electrical and electronic systems.

## Slide 3: What is a diode?
A diode is a semi-conductor.
It has two terminals, the anode and the cathode.
It typically allows the flow of current in one direction only. It has low resistance in one direction, and high resistance in the other.
A key application of diodes is to steer current to flow in the required direction.

## Slide 4: Properties and applications of diodes and transistors
AC
Half wave rectified DC
Full wave rectified DC
V
t
V
t
V
t
One application of diodes is in switching from power coming from a power supply to power running from a battery.
A battery is a device which converts chemical energy into electrical energy in the form of DC voltage. The major drawback with batteries is that they require charging. The charging DC current is usually supplied by an AC source. However, the AC source has to be converted or rectified to DC before connection to the battery can be made.
The illustration above shows an AC waveform and two types of DC waveform, called half and full wave rectification.

## Slide 5: Diodes and rectifiers
Rectifiers are circuits which, in their basic form, are made up of either one diode, which gives half wave rectification, or four diodes, which give full wave rectification. The symbol for a diode is shown below.
Symbol
Diode
Anode +ve
Cathode -ve

## Slide 6: N-type and P-type
A diode is a semiconductor usually made of silicon. It is chemically changed to control its electrical properties, a process called doping. In silicon doping there are two types of impurities added.
N-type: in N-type silicon there are extra electrons, creating a negative charge.
P-type: in P-type silicon an effect of positive charge is created with the absence of an electron creating a positive ‘hole’ (electrons can then occupy the hole).
When you put N-type and P-type silicon junctions together, a diode is created. It will allow current to flow in one direction only.

## Slide 7: P-N junction
Imagine that you connect the positive (+ve) of a battery to the P-side (anode) and the negative (-ve) to the N-side (cathode). The holes from the P-side are repelled by the +ve connection and the electrons in the N-side are repelled by the -ve connection.
This causes a reduction in the depletion layer as atoms at the junction can now pass off charges to one another, and current flows.
If you connect the +ve to the N-side and the -ve to the P-side then the free charges are now attracted to the +ve and -ve connections and the depletion layer widens, preventing current flow.

## Slide 8: Current flow through a diode
0.3V
0.7V
100
Diode characteristics
Forward bias
Reverse bias
200
300
IF
IR
VR
VF
Si
Si
The graph shows the current flow through a diode in the forward bias direction, ie +ve to the P-side and -ve to the N-side.
It only requires about 0.7V across the diode for current to flow.
The reverse bias is shown, ie +ve to the N-side and -ve to the P-side. This prevents current flow, however if the voltage is raised high enough the diode will conduct and this can damage the device (PIV).
Peak inverse voltage (PIV)

## Slide 9: Half wave rectification
V ac
On the positive half cycle of AC, the diode is forward-biased and current flows through the resistor. On the negative half cycle, the AC current has reversed so the diode is reversed-biased and blocks the flow of current.
I dc
Vdc
Vpk
Vdc = 0.318Vpk

## Slide 10: Full wave rectification
When terminal 1 is +ve and terminal 2 is -ve, diodes D1 and D4 conduct while D2 and D3 block.
When terminal 2 is +ve and terminal 1 is -ve, D2 and D3 conduct whilst D1 and D4 block.

## Slide 11: Transistors
A transistor can be considered to be a three-connection P-N junction.
They commonly come in two designs: NPN and PNP.
The three connections are called the base, collector and emitter.
The symbols for the devices are shown opposite. The emitter always has the arrow on its symbol and the arrow always points to the N region of the junction.
n
p
n
p
n
p
Collector
Base
Emitter
Collector
Base
Emitter

## Slide 12: Types of transistor
A transistor’s construction can be microscopic in size to fit on microchips, to allow equipment such as mobile phones to be small in size. Transistors can also be large water-cooled devices to control large power installations. The operation however is very similar in each case.
A transistor can regulate or control voltage and current flow in addition to amplifying these variables. It can also act as a switch between two states (on or off).
Collector (c)
Emitter (e)
Base (b)
NPN transistor
Collector (c)
Emitter (e)
Base (b)
PNP transistor

## Slide 13: How transistors work
Transistors work by applying a small voltage on the base with respect to the emitter (about 0.7V). Current will then flow between the collector and emitter.
The current flow will be larger between the collector and emitter than the current supplied to the base, so the transistor is acting as an amplifier. Remove the base supply and the transistor switches off.
The operation of NPN and PNP are similar, however the polarity of the voltages on each connection and the flow of current is different.
Single transistor
CPU with millions of transistors installed

## Slide 14: Amplifiers
Ic
Ie
NPN transistor
Collector(c)
Emitter(e)
Make base –ve 0.7V
PNP transistor
Make base +ve 0.7V
The NPN transistor has the base +ve with respect to the emitter and the transistor turns on. The current flowing between collector and emitter is larger than the base current. This is the current gain of an amplifier.
The PNP transistor has the base -ve with respect to the emitter and the transistor turns on. The current flowing between emitter and collector is in the opposite direction.

## Slide 15: Applications of transistors
Transistors are popular as a switch. Because as they have no mechanical parts, they can switch very quickly (over 100 million on/off cycles a second). They are less prone to breakdown as a result.
They can amplify small currents (uA to mA) in musical applications. You can then cascade (connect in series) more amplifiers to achieve the power outputs from large speakers at music festivals and similar events.
In marine applications, transistors are used to regulate the current to propulsion drives on big cruise ships.

## Slide 16: Temperature considerations
Semiconductor components are sensitive to temperature. When these devices are used for high power applications, the temperature must be managed. A mechanical switch has zero volt drop across it, so no power loss is experienced.
When diodes and transistors are conducting current they have small voltage drops across them. When the current is large the power loss can be in the kilowatt (kW) levels, which would destroy the device unless the internal heat is removed. This can be achieved through forced air cooling or water cooling.
Transistors
Water cooled heatsink

## Slide 17: Measuring water conductivity
The water purity must be exceptionally high as this increases its electrical resistance and avoids short circuits with other connected transistors.
The conductivity of the water is measured by instrumentation. If its conductivity increases, the devices can be tripped off. The unit of conductivity is microsiemens (μS) with acceptable values of below 5uS.

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.