## Slide 1: PowerPoint 1: Mechanical components
PowerPoint presentation
9. Mechatronics
9.1 The key components of a mechatronics system

## Slide 2: Objectives
By the end of this session learners should be able to:
define a mechatronic system
describe the key mechanical components of a mechatronics system:
  gears
  cams and followers
  linkages
  levers
  pulleys.

## Slide 3: What is mechatronics?
Mechatronics is the integration of mechanical and electronic systems to produce a functioning system.
Mechatronic systems are therefore made up of both mechanical and electronic components.
Examples of mechatronic systems include:
  robotic arms
  computer numerical control (CNC) machines
  automated locking systems
  car anti-lock braking systems
  moving camera systems.

## Slide 4: Gears
  Gear ratio = number of teeth on driven gear/number of teeth on driver gear.
  The gear ratio must be expressed as a ratio (eg 3:1), not just a number.
Gears are toothed wheels that are arranged in gear trains to increase or decrease speed and torque.
A larger gear driving a smaller gear increases speed but reduces torque.
A smaller gear driving a larger gear increases torque but decreases speed.
This is represented by calculating the gear ratio.
Two gears in a train.

## Slide 5: Cams and followers
Cams and followers turn rotary motion into reciprocating motion.
  Rotary motion is motion in a circle.
  Reciprocating motion is motion that goes back and forth.
As the cam rotates it pushes the follower up and down. The cam can be turned by hand or automatically using an electric motor.
Cams come in a range of different shapes, each affecting the motion of the follower in a different way.

## Slide 6: Gears and cams
Cam shaft
Gear wheels

## Slide 7: Linkages
Commonly used linkages in mechanical and mechatronic systems include:
  reverse motion linkages (shown right)
  parallel motion linkages
  bell cranks.
Linkages are used to change the type or direction of motion, and/or the size of a force.
Rods are joined together via fixed or moveable pivots that either restrict or allow their movement.
Fixed pivot
Moving pivot
Moving pivot

## Slide 8: Levers
There are three main types of lever used in mechanical systems:
  1st class lever, eg a seesaw or a pair of scissors
  2nd class lever, eg a wheelbarrow or car door
  3rd class lever, eg a broom or fishing rod.
Levers are used to move a big force using a smaller, effort force. Levers are constructed using a rigid rod that turns on a pivot.
Fulcrum
Effort
Load
Scissors are an example of a 1st class lever

## Slide 9: Pulleys
  mechanical advantage = load force/effort force
  It is expressed as a simple number, eg 3.
Pulleys are used to reduce effort when lifting loads.
They do this by using wheels, an axle and a rope to increase the mechanical advantage.
The mechanical advantage of a pulley is its ability to lift a large load with a small effort force.
This is calculated using the formula:

## Slide 10: You turn
Parallel motion linkages
Bell crank
  Reverse motion linkages
  Investigate how each of these linkage types changes the type/direction of motion and the size of a force.
Notes: Images used with permission of Engineerfix.com (https://engineerfix.com/a-complete-guide-to-linkage-mechanisms/).

## Slide 11
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.