## Slide 1: PowerPoint 10: Hydraulic and pneumatic components
PowerPoint presentation
9. Mechatronics
9.3 The basic principles of hydraulics and pneumatics

## Slide 2: Objectives
By the end of this session, learners should be able to:
outline the form and function of the following hydraulic and pneumatic components:
  pumps
  compressors
  valves
  actuators
  cylinders.
Pneumatic compact air cylinders
Notes: The picture shows.

## Slide 3: Pumps
Pumps are devices that convert electrical or mechanical energy into hydraulic energy.
The purpose of a pump is to create fluid flow by overcoming the pressure induced by a resistive load.
Pump symbol
Axial piston hydraulic pump

## Slide 4: Compressors
Compressors perform a similar function in pneumatic systems by converting electrical or mechanical energy into pressurised air.
Compressors can be categorised in terms of the pressure they can deliver – high, medium and low.
Compressor symbol

## Slide 5: Valves
In fluid power systems, valves control the direction of the fluid.
Hydraulic valves are actuated by a liquid, such as water or oil.
  Pneumatic valves are actuated by compressed air.
  In each case, this in turn allows the valves to control the movement of cylinders, actuators and even other valves.
Pneumatic solenoid valve assembly

## Slide 6: Connecting valves with simple fluid power logic circuits
Simple fluid power logic circuits can be created by connecting valves in different arrangements:
  an AND circuit is created by connecting two valves in series
  an OR circuit is created by connecting two valves in parallel.

## Slide 7: Actuators and cylinders
Actuators turn the hydraulic or pneumatic energy within a system back into mechanical energy. Cylinders are actuators that use fluid power to force a piston to move in a certain direction.
  A piston rod moves back and forth within a barrel to create the movement.
  The output force of a cylinder can be calculated by using the formula: force (F) = pressure (P) x area (A), where A = πr2 and r is the radius of the cylinder.

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.