## Slide 1: PowerPoint 4: Drive devices
PowerPoint presentation
9. Mechatronics
9.1 The key components of a mechatronics system

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe common drive devices in mechatronics systems, including:
  standard electrical motors
  servo motors
  stepper motors.
AC servo motor, DC brush-less motor, and stepping motor.

## Slide 3: Standard electrical motors
Motors convert electrical energy into movement.
A standard DC motor creates rotary movement when a direct current flows through it.
If the direction of current is reversed, so is the direction of rotation. When a motor works in reverse it acts as a generator.
The speed of a direct current (DC) motor can be controlled by varying the supply voltage or by changing the strength of current in its field windings.
Solar motors are small, cheap DC motors that can run directly from solar panels.
The circuit symbol for a motor is shown on the right.
M

## Slide 4: Servo motors
Servo motors turn through a precise angle, which is controlled by a series of pulses.
  The width of the pulses controls the angle through which it turns.
  A microcontroller is often used to provide these pulses via a suitable motor driver circuit.
Servo motors are used when precise position, acceleration and/or velocity control are required.
Servo motors are commonly used in robotics applications and computer numerical control (CNC) machinery.

## Slide 5: Stepper motors
Stepper motors turn through precise steps.
This is achieved by dividing each full rotation into a sequence of equal steps. A suitable motor driver circuit is required for successful operation.
Servo motors are used when something needs to be moved through an exact angle or distance.
Servo motors are commonly used in precision movement equipment such as moving cameras, CNC machinery and printers.

## Slide 6
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.