## Slide 1: PowerPoint 2: Process blocks
PowerPoint presentation
Engineering and manufacturing control systems
10.1 Principles and applications of control system theory

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the part processes play in control systems
describe different process devices (timers, comparators, pulse units, counters and latches).

## Slide 3: Processes
Control systems consist of different input, process and output blocks.
  A process can take an electrical or electronic signal from the input block and alter it some way. For example:
  making it high or low for a set period of time, or until it is reset
  comparing it with another signal
  turning it into a series of pulses
  counting the number of signals or pulses received.
  What devices can you think of that act as processes in control systems? What are their applications?
Notes: Devices for discussion could include timer ICs, comparators/amplifiers, pulse units, counter ICs and latches. Applications could include warning/alarm timers, audio amplifiers, light/temperature control systems, automated stock/production counters and pulse generators for electronic testing equipment.

## Slide 4: Processes in block diagrams
Processes are generally shown in the middle of a block diagram, after the input blocks and before the output blocks.
  The arrows represent the signals flowing in and out of the block, whereas the block represents the process function or device itself.
Process
Electrical signal
Electrical signal

## Slide 5: Types of process device
There are several types of process device used in control systems.
  Timers take a signal and keep it high or low for a set period of time. The time period can often be adjusted by changing component values, such as by using a resistor–capacitor (RC) network.
  Comparators compare a signal received with a reference signal to see which is bigger or smaller.

## Slide 6: Types of process device
  Pulse units produce a continuous series of digital pulses. The time over which each pulse is high or low can usually be adjusted.
  Counters add up the number of signals or pulses they receive. This information can then be displayed using an output device, such as a digital screen.
  Latches keep a signal high or low until they are reset (eg using a reset switch).

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.