## Slide 1: PowerPoint 3: Logic gates
PowerPoint presentation
Engineering and manufacturing control systems
10.1 Principles and applications of control system theory

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the purpose of function of AND, OR and NOT logic gates.

## Slide 3: Logic gates
Logic gates are digital process devices that respond to and emit (output) signals that are either high or low.
  High signals are represented by logic 1, low signals by logic 0.
  Truth tables are used to show the output signals each type of logic gate produces for given input signals.
  You need to understand how AND, OR and NOT gates function when used in control systems.
  What applications can you think of that might use logic gates in a manufacturing control system context?
Notes: Applications for discussion could include sorting materials and parts on a production line, alarm and warning systems used in quality control (eg if incorrect measurements are detected) and lifting systems for products that are being prepared for distribution.

## Slide 4: AND gates
  AND gates produce a high (1) output signal when both input signals are high (1).
  They produce a low (0) output signal when either or both input signals are low (0).
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Input B
Output
Input A
Truth table

## Slide 5: OR gates
  OR gates produce a high (1) output signal when either or both input signals are high (1).
  They produce a low (0) output signal when both input signals are low (0).
Truth table
Input A | Input B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Input B
Output
Input A

## Slide 6: NOT gates
  NOT gates produce a high (1) output signal when the input signal is low (0).
  They produce a low (0) output signal when the input signal is high (1).
Truth table
Input | Output
0 | 1
1 | 0
Input
Output
Notes: NOT gates are often referred to as inverters.

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.