## Slide 1: PowerPoint 7: Representing control systems
PowerPoint presentation
Engineering and manufacturing control systems
10.1 Principles and applications of control system theory

## Slide 2: Objectives
By the end of this session, learners should be able to explain the differences between:
system block diagrams
schematics
wiring diagrams.

## Slide 3: System block diagrams
As you learned earlier, block diagrams show an overview of control systems in terms of their input, process and output functions, and subsystems.
The blocks represent the components or groups of components that make up each function or subsystem. The arrows represent the signals that flow between them. The diagram shows a block diagram for a light sensing alarm.
Light sensor
Input
Process
Output
Timer
Buzzer
Light
level
Sound

## Slide 4: Schematics
Schematics show the individual components in a circuit or system and how they are connected together.
Standard circuit symbols are used to represent the components and wiring connections (BS 3939). The diagram shows a schematic for a resistor–capacitor (RC) timer circuit.

## Slide 5: Pros and cons of schematics
The use of standard circuit symbols in schematics means that anyone can interpret them. Because symbols can be made smaller than pictures of components, diagrams are easier to understand, and can be produced to a manageable size – especially useful in giving an overview of complex systems.
However, unlike wiring diagrams, schematics do not show the physical layout of the components and wiring, which means the engineer cannot see where they will be placed in the casing.

## Slide 6: Wiring diagrams
Wiring diagrams show both the physical connections and the physical layout of a circuit or system.
Simple pictorial representations of components are shown along with the wires that connect them together. This helps engineers to perform installations and fix faults.
The diagram shows the wiring for an RC timer circuit. Compare this to the schematic shown on slide 4.

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.