## Slide 1: PowerPoint 9: Sensors and actuators
PowerPoint presentation
Engineering and Manufacturing Control Systems
10.2 How sensors and actuators are used in automation control systems

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the different types of sensors and actuators
explain the different applications of sensors and actuators.
Notes: Picture shows a rear parking (proximity) sensor.

## Slide 3: Types of sensor
Sensors are used to monitor changes in the environmental conditions around them.
Analogue sensors produce continuous output signals. These are usually in the form of a voltage that is proportional to the quantity being measured.
Digital sensors produce discrete output signals (eg in the form of 1s for high signals and 0s for low signals).
Active sensors transmit a signal into the environment and measure the response that comes back from it (eg an infrared proximity sensor).
Passive sensors monitor the changes that are happening in the environment around them (eg a temperature sensor).

## Slide 4: Types of actuator
Actuators are devices that turn an electrical, mechanical or environmental signal into a physical movement (eg a motor produces rotary movement when an electrical current flows through it).
Analogue actuators produce and/or respond to continuous output signals.
Digital actuators produce and/or respond to discrete output signals.
Active actuators either introduce new energy into a system and/or require an external energy supply.
Passive actuators do not introduce new energy into a system and do not require an external energy supply.

## Slide 5: Applications of sensors and actuators
  Switching systems (eg for machine safety control).
  Proximity sensing (eg for vehicles and automation systems).
  Laser sensing (eg when measuring the dimensions of products on a production line).
  Vision systems (eg in robotics applications).
Sensors and actuators are used in a wide range of different control system applications.
Notes: Picture shows an automated robot arm.

## Slide 6: Signal transmission and power
Sensors and actuators can be connected to other components via wires and cables (hard-wired) or via wireless systems such as Wi-Fi and Bluetooth.
Some systems make use of both wireless and hard-wiring to transmit signals.
Sensors and actuators requiring an electrical power supply can be powered using batteries, AC adapters and so on, in order to provide the required voltage for the system.

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.