## Slide 1: PowerPoint 4: Control and management
PowerPoint presentation
11. Quality management
11.1 Quality standards, assurance, control and improvement

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the main principles, purposes and outcomes of quality control (QC).
understand the function and purpose of inspection
understand what process capability is
describe the advantages and disadvantages of 100% sampling compared to statistical process control (SPC)
be familiar with the use of Six Sigma for high volume manufacture.

## Slide 3: Quality control (QC)
Quality control (QC) implements the quality assurance inspection and testing requirements.
An organisation will often begin by testing raw materials, pulling samples from along the manufacturing line and testing the finished product.
Testing at the various stages of the manufacturing process helps to identify where a production problem is occurring and the remedial steps required to prevent it happening in the future.
QC ensures that the final product meets the requirements.

## Slide 4: Purposes of inspection
To distinguish good lots from bad lots.
To distinguish good pieces from bad pieces.
To determine if the process is changing.
To determine if the process is approaching the specification limits.
To rate the quality of the product.
To rate the accuracy of inspectors.
To measure the precision of the measuring instrument.
To secure products – design information.
To measure process capability.

## Slide 5: Stages of inspection
Inspection of incoming materials
Also called receiving inspection, this stage involves inspecting and checking all the purchased raw materials and parts that are supplied before they are taken into the stock or used in actual manufacturing.
2. Inspection of the production process
The work of inspection is done during the production process. Inspection is carried out at various work centres and at the critical production points.
3. Inspection of finished goods
This is the last stage when finished goods are inspected and tested before marketing to ensure that poor quality products are either rejected or sold at reduced prices.

## Slide 6: Types of inspection
There are two methods of inspection:
100% sampling
statistical process control (SPC).
Inspection
Statistical process control (SPC)
Sampling inspection
100%
inspection

## Slide 7: 100% sampling
The method of 100% sampling is a very detailed inspection of the quality at each strategic point or stage of manufacture, where the test involved is non-destructive and every piece is separately inspected.
It requires more inspectors and hence is a costly method.
There is no sampling error but inspector fatigue may be a weakness.
It is suitable only when a small number of pieces are required to be inspected or when a very high degree of quality is required.
Examples of 100% sampling include inspection of jet engines and aircraft, and medical and scientific equipment.

## Slide 8: Statistical process control (SPC)
Statistical process control (SPC) is a method of quality control which employs statistical methods to measure, monitor and control a process (ie sampling).
This helps to ensure that the process operates efficiently, producing more specification-conforming products with less waste (rework or scrap).
An advantage is that it emphasises early detection and prevention of problems, rather than the correction of problems after they have occurred.

## Slide 9: Control chart
One typical SPC method is to use a control chart. This shows how product sample values vary over time. The centre line is the average output.

## Slide 10: Advantages and disadvantages of 100% sampling vs SPC
 | 100% sampling | SPC
Cost | Expensive to operate | Cheaper to operate
Time | More inspection time required | Can be automated at very high speed
Fatigue | Inspectors may suffer from fatigue | Inspector fatigue mainly eliminated
Staff | More staff required | Less staff required as can be automated
Damage | More damage to products due to more handling | Less damage to products due to minimal handling
Destructive testing | Cannot be carried out | Can be carried out
Product lot | Lot may be saved as each piece is sampled | Entire lot may be rejected if a sample is found defective
100% sampling is used for high value and safety critical products. SPC is typically used for products manufactured at high speed.

## Slide 11: Process capability
Process capability is a statistical measure of the repeatability and consistency of a manufacturing process relative to customer requirements. In other words ‘How can the process produce products to meet customer specifications?’
It defines specification limits by using a lower specification limit (LSL) and an upper specification limit (USL).
Lower
specification
limit (LSL)
Upper
specification
limit (USL)
In this example, the garage defines customer specification limits and the car size represents the process limits.
If the car is smaller than the garage, it means the car will fit in the garage.
Therefore when the data (car) is smaller than the specification limits (garage), the process is capable.

## Slide 12: Six Sigma for high volume manufacture
Six Sigma is a method for reducing defects of any kind in a given process.
It originated at Motorola in the 1980s but has been adopted in organisations in manufacturing, engineering, construction and supply chain management.
It has been highly successful in reducing costs in large manufacturing companies globally.

## Slide 13: The benefits of Six Sigma
The motive of every business is to satisfy its customers and make a profit. This motive can be addressed by reducing:
the time, to improve the output of products
the defects, so the business can reduce waste, produce more products and increase profit
variation in the process, so the business can provide products that meets the customer’s specifications every time.

## Slide 14: Six Sigma: the DMAIC methodology
Introduced in PowerPoint 3, Six Sigma uses the DMAIC methodology:
Define
Measure
Analyse
Improve
Control
You will recognise this as the ‘right first time’ approach discussed in PowerPoint 3, and already be familiar with the graphic on the next slide.

## Slide 15: DMAIC methodology
Define the problem
What is wrong with a process?
Measure the problem
What is the magnitude of the problem?
Analyse the root cause
Improve the process
Eliminate the root cause and implement process changes
Control the process
Control the process by regular reviews
What is the root cause of the problem?

## Slide 16
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.