## Slide 1: PowerPoint 5: Quality improvement
PowerPoint presentation
11. Quality management
11.1 Quality standards, assurance, control and improvement
Notes: Image source: Getty images: Monty Rakusen: 664661747

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the main principles, purposes, advantages and disadvantages of the different approaches to quality improvement:
  – failure mode and effect analysis (FMEA)
  – quality circles
  – Pareto analysis
  – cause and effect diagrams.

## Slide 3: Quality improvement
Quality improvement is a systematic approach using specific methods to improve quality, thereby achieving successful and sustained improvement. The model for quality improvement is the PDSA cycle.
What needs to be accomplished?
How will a change be identified as an improvement?
What changes can be made that will result in an improvement?

## Slide 4: Failure mode and effect analysis (FMEA)
Failure mode and effect analysis (FMEA) is a structured way to identify and address potential problems or failures, and their resulting effects on the system or process, before an adverse event occurs. What can go wrong in the process?
Failure
Potential
Mode
Types, ways, possibilities
Effect
Negative effect on process
Analysis
Assess risk and reduce it

## Slide 5: FMEA
Results of the analysis might be recorded in an FMEA spreadsheet.
FMEA is widely used in manufacturing industries in various phases of the product life cycle to ensure reliability.
It allows early identification of potential failure points in a system, which can be documented and ranked by how critical they would be for the manufacturing process.
FMEA is the process of reviewing systems to identify potential failure modes and their causes.
Effects analysis studies the consequences of those failures on different system levels.

## Slide 6: FMEA
Advantages | Disadvantages
Can be used for existing and new products | Evaluation is often subjective
Enables actions to be prioritised | Evaluation can vary between teams
A good communication tool | Time consuming
Clarifies the magnitude of risks and actions | Solutions can be so large and complex they become impossible to manage

## Slide 7: Quality circles
Quality circles are small groups of workers of different levels in the firm who come together to discuss and solve problems in production.
Managers, assembly line workers and engineers mix together and everyone’s opinion is valued and respected. Membership of quality circles is voluntary.

## Slide 8: Quality circles
Advantages | Disadvantages
Increased productivity | Inadequate training
Improved quality | Unsure of purpose
Employee morale boost | Lack of management interest
 | Quality circles are not really empowered to make decisions

## Slide 9: Pareto analysis
Pareto analysis is a decision-making tool which is useful where many possible courses of action are competing for attention.
Pareto analysis estimates the benefit delivered by each action, then selects a number of the most effective actions that deliver a total benefit reasonably close to the maximal possible one.
The 80/20 rule (also known as the Pareto principle) states that, for many events, roughly 80% of the effects come from 20% of the causes.
For example, 80% of car accidents are caused by 20% of motorists or 20% of tools in the toolbox are used for 80% of tasks.

## Slide 10: Pareto analysis chart
A Pareto analysis chart shows the frequency of any defects and the cumulative percentage of them happening. An 80% line is drawn to work out the 20% of defects that need attention.

## Slide 11: Pareto analysis
Advantages | Disadvantages
Clearly shows the significant and insignificant variables | May need more than one chart
Allows determination of which problem to address first | Only shows qualitative data, cannot use it to calculate, mean, average or other statistics that may be needed
Can help working with limited resources since the data is displayed hierarchically | Does not identify what is causing the problem that is being analysed

## Slide 12: Cause and effect diagrams
A cause and effect diagram, also known as an Ishikawa or ‘fishbone’ diagram, is a graphic tool used to explore and display the possible causes of a certain effect.
The diagram breaks down the causes of the problem into discrete branches, helping to identify the main or root causes.
Problem
Machines
People
Methods
Materials
Measurements
Environment
Causes

## Slide 13: Cause and effect diagrams
Advantages | Disadvantages
Provide a visual structure for considering influences on performance | Tend to be simplistic for real-world problems
Cause and effect diagrams are easily constructed and understood | The data, which may not have been verified, may lead to inappropriate improvement strategies being implemented
Allow more reliable improvement strategies to be developed | Not everyone feels comfortable with the diagram format
Allow decision-makers to brainstorm ideas in a systematic and logical way | Must be used with other decision-making methods to establish the root causes of a problem

## Slide 14
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.