## Slide 1: PowerPoint 7: Environmental legislation
PowerPoint presentation
12. Health and safety principles and coverage
12.6 Principles and practices relating to environmental legislation and considerations

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the main requirements of the current key environmental legislation within the engineering industry
outline the legislation that should be satisfied by a company's environmental policies.

## Slide 3: Regulating pollution and the environment
There are numerous environmental laws in the UK that cover everything from fly-tipping, littering and pollution to wildlife, conservation, climate change, noise and planning. This presentation covers the following legislation:
Pollution Prevention and Control Act 1999
Clean Air Act 1993
Environmental Protection Act 1990
Dangerous Substances and Explosive Atmospheres Regulations (DSEAR) 2002
Radioactive Substances Act 1993
Controlled Waste Regulations 2012
Hazardous Waste Regulations 2005

## Slide 4: DEFRA
In England, the main body responsible for developing environmental policy and legislation is the Department for Environment, Food and Rural Affairs (DEFRA).
Employers are legally responsible for ensuring that all environmental regulations are complied with.
However, as an employee, you should also be familiar with the key legislation, understand why it is needed and who is responsible for compliance.

## Slide 5: Pollution Prevention and Control Act 1999
The Pollution Prevention and Control Act 1999 requires industrial activities with high pollution potential to have an environmental permit and meet environmental conditions.
It covers such areas as:
waste
water quality
air quality
environmental noise.
Pollution Prevention and Control Act 1999 (legislation.gov.uk)

## Slide 6: Clean Air Act 1993
The Clean Air Act 1993 covers all potential sources of air pollution. As such it places controls on smoke emissions and imposes restrictions such as the height of chimneys, along with all emissions relating to transport.
Clean Air Act 1993 (legislation.gov.uk)

## Slide 7: Smoke control under the Clean Air Act
The Clean Air Act controls domestic and industrial smoke emission.
It makes it an offence to cause or permit the emission of dark smoke from a chimney or flue at industrial or trade premises.
This also applies to burning materials on a site that you own or a site where you are working such as a building or demolition site.
Under the act, local authorities must approve chimney heights for furnaces burning certain types of fuel at high rates.
The act also introduced ‘Smoke Control Areas’ in order to control emissions produced from domestic houses by ensuring only clean fuel is burned in those areas.

## Slide 8: Environmental Protection Act 1990
The Environmental Protection Act 1990 was designed to improve the control of pollution of the air, water and land by regulating the management of waste and the control of emissions.
It imposes a duty of care on any business or person who produces, carries, keeps, treats, disposes of or imports controlled waste to do so safely.
Environmental Protection Act 1990 (legislation.gov.uk)

## Slide 9: Environmental Protection Act
Waste management in engineering
Any waste generated on site will normally need to be stored for a period of time before collection. Employers have a legal responsibility to ensure waste is stored safely. Regulations require the following actions.
  Pre-treatment – ie sorting recyclable and non-recyclable material. This can be onsite or completed by a registered waste collector at a sorting facility.
  Safe onsite storage for all waste.
  Waste must be collected by a registered waste carrier.
  Disposal of waste must take place at a licensed waste disposal facility.
  Waste must be covered by a waste transfer note.

## Slide 10: Dangerous Substances and Explosive Atmospheres Regulations (DSEAR) 2002
  A dangerous substance is any substance present at work that could, if not properly controlled, cause harm to people as a result of a fire, explosion or corrosion of metal, including:
  solvents, paints, varnishes
  flammable gases, such as liquid petroleum gas (LPG)
  dust from machining and sanding operations
  dust from foodstuffs
  pressurised gases
  substances corrosive to metal.
  Dangerous Substances and Explosive Atmospheres Regulations 2002 - Fire and explosion (hse.gov.uk)

## Slide 11: What does DSEAR require?
Employers must:
identify dangerous substances in their workplace and what the risks are
introduce control measures to either remove those risks or control them
implement controls to reduce the effects of any incidents involving dangerous substances
prepare plans and procedures to deal with accidents, incidents and emergencies
ensure employees are properly informed and trained to deal with the risks
classify areas of the workplace where explosive atmospheres may occur and avoid ignition sources (eg unprotected equipment) in those areas.

## Slide 12: Controlling radioactive and other types of waste
  Radioactive Substances Act 1993
  Concerned with the control of radioactive material and the disposal of radioactive waste.
  Radioactive Substances Act 1993 (legislation.gov.uk)
  Controlled Waste Regulations 2012
  Household, industrial and commercial waste are classed as controlled waste and are subject to the Environmental Protection Act 1990.
  The Controlled Waste (England and Wales) Regulations 2012 (legislation.gov.uk)
  Hazardous Waste Regulations 2005
  Waste is considered ‘hazardous’ under environmental legislation when it contains substances or has properties that might make it harmful to human health or the environment.
  Hazardous Waste (England and Wales) Regulations 2005 (legislation.gov.uk)

## Slide 13: Your turn
PowerPoint presentation
  Carry out some research online to identify the key waste areas covered by the Hazardous Waste Regulations 2005 (Section 3).
  Find out what other regulations are referred to for each type of waste and make a list.
Notes: Source: https://www.bbc.co.uk/news/science-environment-61350996

## Slide 14
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.