## Slide 1: PowerPoint 2: 8 wastes
PowerPoint presentation
16. Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
understand what waste is
describe Toyota’s ‘8 wastes’.

## Slide 3: Lean manufacturing
  In engineering, all activities have a cost. This may be money, space or time.
  Activities can be classified as either:
        value-added: these increase the value of the product in some way
        non-value-added: these do not change the value of the product to the company or customer.
  ‘Lean manufacturing’ is production with the minimum possible amount of non-value-added activities.
  By reducing the quantity of non-value-added activities, companies can reduce their costs.

## Slide 4: Toyota’s ‘8 wastes’
  The car manufacturer Toyota was the first to refer to non-value-added activities as waste.
  They classified waste into eight different types – the ‘8 wastes’:
        transportation
        inventory
        motion
        waiting
        excess production (overproduction)
        overprocessing
        defects
        unused talent.

## Slide 5: Transportation
  Transportation is the unnecessary movement of materials. For example, moving parts twice between processes.
  Movement takes labour time, which must be paid for.
  It may also require equipment such as cranes, forklift trucks and conveyor belts.
  More transportation = more labour time + more equipment = more cost.
  Movement can be reduced by putting processes next to each other, so parts flow directly from one process to another

## Slide 6: Inventory
  Inventory refers to any materials that are not currently being processed.
  This includes raw materials and finished goods – these cost money and need space to be stored.
  Companies borrow money to buy materials – they have to pay it back with interest.
  More inventory = more money borrowed = more interest to pay = more cost.
  Inventory can be reduced by using ‘just-in-time’ manufacturing or flowing materials direct from process to process

## Slide 7: Motion
  The waste of motion is any unnecessary movement by people.
  For example, hunting for misplaced tools, workers having to bend and twist to pick up parts.
  Motion takes time and effort by people.
  More motion = more labour time = more cost.
  Motion can be reduced by the effective design and management of processes

## Slide 8: Waiting
  The waste of waiting means the time materials spend between processes.
  In a similar way to inventory, companies borrow money to buy materials and they have to pay this money back with interest.
  More waiting materials = more money borrowed = more interest to pay = more cost.
  Waiting can be reduced by flowing materials direct from process to process

## Slide 9: Excess production (overproduction)
  Excess production or overproduction means making more products than the customer needs.
  This might be, for example, to provide spares in case of quality problems.
  In a similar way to inventory, companies borrow money to buy materials for production and have to pay this money back with interest.
  More materials = more money borrowed = more interest to pay = more cost.
  Excess production can be reduced by only making products when the customer needs them and only making the quantity needed

## Slide 10: Overprocessing
  Overprocessing is producing work that is of a higher quality than needed.
  For example, working to a tighter tolerance or adding features that the customer doesn’t need.
  Overprocessing = more labour time = more cost.
  Overprocessing can be reduced by understanding customers’ needs and doing only what is required to meet those needs

## Slide 11: Defects
  Defects refers to any products or aspects of products that do not meet the expectations of customers.
  Defects are often identified by quality checks.
  It takes labour time (and therefore cost) to inspect products and fix defects.
  Defects = labour costs for inspection and rectification + replacement materials = more cost.
  Defects can be reduced by making the product right first time

## Slide 12: Unused talent
  Unused talent is also called waste of skills.
  This means not making full use of the skills and knowledge of workers.
  Workers often have a better understanding of what they do than anyone else – and what needs to be changed to make things better or easier.
  This is not an extra cost – the workers are being paid anyway, so it is a missed opportunity.
  The waste of unused talent can be reduced by giving all workers opportunities to contribute to improving performance

## Slide 13: How to remember the different types of waste
The types of waste can be remembered using the acronym TIMWOODS.
 | Type of waste
T | Transportation
I | Inventory
M | Motion
W | Waiting
O | Overproduction (excess production)
O | Overprocessing
D | Defects
S | Skills of workers (unused talent)

## Slide 14
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.