## Slide 1: PowerPoint 3: Key performance indicators
PowerPoint presentation
16. Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the meaning of the term ‘key performance indicators’ (KPIs)
describe the different types of KPI.

## Slide 3: Evaluating current performance
  The first step towards improving performance is to evaluate current performance. This allows companies to:
identify areas where there is the most potential to eliminate waste and improve performance
compare the performance of similar processes
compare their performance to that of competitors.

## Slide 4: What are key performance indicators?
  Key performance indicators (KPIs) are quantifiable measures of performance.
  They might relate to a single manufacturing process, a series of processes or the whole business.
  Most companies will use a range of different KPIs, to give a broad picture of their performance.

## Slide 5: Types of KPI: individual processes
KPI | What it measures | Example
Cycle time | The time to machine one item in a process | 2.3 minutes
Changeover time | Time to switch a process between making different products | 90 minutes
Throughput | Number of products manufactured per unit time | 24
Operating equipment effectiveness (OEE) | (Number of good products made x ideal processing time / planned production time) x 100 | Products/hour 60%
  The following measures are most commonly used to evaluate the performance of a single process.

## Slide 6: Types of KPI: groups of processes
KPI | What it measures | Example
Throughput | Number of products manufactured per unit time | 320 units/week
Total cycle time | Sum of the actual machining time of the different processes needed to manufacture the product | 48 minutes
On-time delivery | (Quantity of products delivered on time / total quantity of products) x 100 | 92%
Lead time | Time to manufacture a customer order from start to finish | 64 days
Capacity utilisation | (Output achieved / potential output) x 100 | 58%
  The following measures are most commonly used to evaluate the performance covering the overall production of a product.

## Slide 7: Types of KPI: quality of output
KPI | What it measures | Example
Scrap | (Total number of products scrapped / total products produced) x 100 | 4%
Yield | (Good products produced / total products produced) x 100 | 96%
  The following measures can be used to evaluate quality of performance for either individual processes or all the stages of production (eg for a production line).

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.