## Slide 1: PowerPoint 5: VSM
PowerPoint presentation
16. Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the analytical method knows as value stream mapping (VSM)
understand why VSM is useful and how to carry it out.

## Slide 3: Ideal performance
  As you learned in the first session, in an ideal world, all manufacturing activities would be performed 100% effectively, and at the minimum possible cost.

## Slide 4: Achievable performance
  However, in the real world this almost never happens because:
  the company only has certain equipment available
  the production area may make different products, each of which has a different ‘optimum’ method or arrangement of equipment
  tools may need to be borrowed by other workers for other tasks
  the working area or the equipment may not be well maintained.
  Therefore, it is always possible to improve manufacturing performance.

## Slide 5: What is VSM?
  Value stream mapping (VSM) is a method for analysing the real flow of materials and information through a company. The ideal flow, with the minimum feasible amount of non-value-added activities, is often called the future state map.
  VSM can be used to identify the ‘8 wastes’, or to compare the actual flows to the ideal flow.
  This information can be used to identify where improvements can be made and which continuous improvement tools would be the most effective to apply.

## Slide 6: Benefits of VSM
        With relatively little effort, VSM highlights areas where improvements can be made.
        Any subsequent continuous improvement activities can be focused to achieve the maximum return on effort.
        It helps to identify the most effective continuous improvement tools.
        Developing future state maps can lead to a complete reorganisation of a business.

## Slide 7: Limitations of VSM
        Each value stream map follows a single product.
        If a company manufactures a wide variety of products, each flow of materials may be different. Multiple different value stream maps may be needed, to ensure that changes for one product do not have a negative effect on other products.

## Slide 8: How is VSM carried out?
  VSM involves physically ‘walking the process’. This tracks the actual route that materials (or information) follow, from arrival at the company to departure of the finished products. Whenever there is an activity, that activity is recorded. One way to do this is to use a VSM form.
  Each activity is classified as either value-added (eg machining a required feature) or as one of the ‘8 wastes’ (eg transportation). The actual map is then compared to the future state map to identify where improvements might be made.
Step no. | Activity | Value-added or non-value-added? | Type of waste
1 |  |  | 
2 … |  |  | 

## Slide 9
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.