## Slide 1: PowerPoint 7: 6S
PowerPoint presentation
16 Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the 6S approach to organisation in the workplace
list the 6Ss (sort, set in order, shine, standardise, sustain, safety), giving examples and describing the benefits of each.

## Slide 3: What is 6S?
  6S is an approach to improving the organisation of a workplace.
  A 6S activity focuses on one working area with the aims of:
        making sure that all required tools and equipment are available
        positioning all tools, equipment and work in progress as conveniently as possible
        removing any items not required for the work activity from the area.
  The 6Ss represent words for each step in the process, each of which has different benefits.

## Slide 4: The 6Ss
6S

## Slide 5: Sort, set and shine
 | 6S | Meaning | Example | Benefits
1 | Sort | Identify items that are needed | Removing any items that are not needed from the workplace | Reduces time taken to find items needed Increases available space Eliminates obstacles
2 | Set in order | Put items in the places that make them most easy to use | Place frequently used items near to where they are used Place all tooling so it is easy to reach | Reduces time taken to find the items needed
3 | Shine | Clean the workplace | Clean machines and equipment Remove any waste products | Makes maintenance issues visible Improves safety

## Slide 6: Standardise, sustain, safety
 | 6S | Meaning | Example | Benefits
4 | Standardise | Establish procedures to ensure the first three Ss are maintained | Implement visual management tools Develop standard operating procedures (SOPs) | Ensures consistent practice in future
5 | Sustain | Ensure good practices are maintained | Ongoing use of visual management tools Ongoing use of SOPs | Maintains the benefits of the first four Ss
6 | Safety | Managing and minimising hazards and risks | Carry out risk assessments and implement control measures | Ensures workers are safe and fewer accidents occur

## Slide 7: Benefits and limitations of 6S
  Benefits:
        a cleaner, more organised workplace where activities should be easier to carry out.
  Limitations:
        requires active participation by the workers in the area
        time is needed to train workers in the approach and then to implement it (typically one to two days for each process area)
        needs ongoing engagement to maintain the benefits.

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.