## Slide 1: PowerPoint 9: OEE and TPM
PowerPoint presentation
16. Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the principles behind operating equipment effectiveness (OEE) and total productive maintenance (TPM)
outline the benefits and limitations of TPM and describe how it is implemented in practice.

## Slide 3: What is OEE?
  Operating equipment effectiveness (OEE) is a key performance indicator (KPI).
  It is a measure of how well an item of equipment is used compared to its potential.
  It is normally presented as a percentage, calculated by:
  (number of good products made x ideal processing time)
  OEE = x 100
  planned production time
  The higher the OEE, the greater the productivity and the lower the unplanned downtime.

## Slide 4: What is TPM?
  Total productive maintenance (TPM) is a philosophy that holds that everyone in the workplace should be involved in maintenance, rather than just the maintenance team.
  The purpose of TPM is to increase the OEE.
  A main feature of TPM is that it uses the experience of operators, as they normally have the best understanding of whether their machine is working well.

## Slide 5: Benefits of TPM
      Less unplanned downtime which results in more productivity and leads to increased income.
      Helps to maintain consistent product quality and more reliable production which can result in increased customer satisfaction.

## Slide 6: Limitations of TPM
        Time is needed to train workers in the approach and implement it.
        Workers need to actively engage with the approach on a continuing basis.

## Slide 7: How is TPM implemented?
  Implementing TPM involves a number of activities – these are often called the eight pillars of TPM.
Notes: IMAGE NEEDS TO BE REDRAWN AS FOUND ONLINE

## Slide 8: The eight pillars of TPM
 | Pillar | Meaning
1 | Autonomous maintenance | Making operators responsible for routine maintenance (eg lubrication, cleaning and inspection)
2 | Focused improvement (kaizen) | Continually improving performance by making small changes
3 | Planned maintenance | Replacing components before they are predicted to fail (ensures continuity of performance)
4 | Quality management | Including error detection and prevention in the production process
5 | Early equipment management | Using operator experience to improve the design of new equipment
6 | Training and education | Ensuring all operators and managers understand TPM
7 | Safety, health and environment | Ensuring the working environment is safe
8 | TPM in administration | Improving administrative tasks (eg order processing, scheduling) to get the best performance out of equipment

## Slide 9
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.